ECEN 5623
Real-Time Embedded Systems
Final Project
Time-Lapse
Ryan Mortenson

Introduction:
This project is a response to the Request For Proposal provided on the ECEN5623 website which requires the system to capture images with an embedded system. The system is comprised of a Nvidia Jetson TK1 and a Logitech C200 camera. The source is written in C and relies on OpenCV and POSIX PThreads libraries with Real-Time Extensions.

Requirements:
Minimum Requirements:
R1: Images shall be acquired from a digital camera at 1 Hz frame rate with resolution of
        640x480.
R2: Images shall be saved in PPM P6 binary format.
R3: Images shall contain uname information in the header as a comment.
R4: Images shall contain time stamp of capture in the header as a comment.
R5: Application shall store the last 2000 images.

Target Requirements:
R6: Images shall be saved in a compressed JPEG Format.
R7: Images shall contain uname information in a COM section of the JPEG.
R8: Images shall contain time stamp in a COM section of the JPEG.
R9: Images shall be transferred via TCP socket to another location for storage.
R10: Remote location shall store more than 2000 images.

Stretch Requirements:
R11: Application shall run at an increased rate of 10 Hz frame rate.

Real-Time Requirements:

The periodicity of the services was determined by the constraints laid out in the Request for Proposal. The minimum and target requirements state that the device must capture images at a 1 FPS, and the stretch requirements must capture a 10 FPS. Since this system is a soft isochronal system and the frame rate is either 1 FPS or 10 FPS the periods were chosen to be 1 second or 100 milliseconds depending on the frame rate. All the services therefore have a 1 second or 100 millisecond deadline and periodicity.
The WCET was determined by running several executions and taking an average of the execution time for each service. To add safety margin the average time was doubled. This should provide enough margin of safety for unexpected delays in the services.

Services:
S1: Scheduler Service: Schedules image capture service.
S2: Capture Service: Captures raw image and passes to JPEG/PPM Service.
S3: JPEG/PPM Service: Translates raw image to PPM or JPEG and writes to file	system. The JPEG service also passes the formatted image to the Server Service.
S4: Server Service (Target and Stretch only): Takes properly formatted JPEG Image and
     sends to client via TCP socket.

Deadlines:
D1: 1 second Minimum and Target, 100 millisecond Stretch
D2: 1 second Minimum and Target, 100 millisecond Stretch
D3: 1 second Minimum and Target, 100 millisecond Stretch
D4: 1 second Minimum and Target, 100 millisecond Stretch.

Execution Times:
C1: 1 millisecond Minimum, Target, and Stretch.
C2: 70 milliseconds Minimum, Target, and Stretch.
C3: 7 milliseconds Minimum, 20 milliseconds (JPEG Compression) Target and Stretch.
C4: 1 millisecond Target and Stretch (No Server Service in Minimum Requirements).

Periods:
P1: 1 second Minimum and Target, 100 millisecond Stretch
P2: 1 second Minimum and Target, 100 millisecond Stretch
P3: 1 second Minimum and Target, 100 millisecond Stretch
P4: 1 second Minimum and Target, 100 millisecond Stretch.

Functional Design Overview and Diagrams:

The time-lapse system was built with an Nvidia Jetson TK1 and the Logitech C200 webcam for image capture. OpenCV was used to interface with the camera, compress JPEG images, and display images with a GUI. The POSIX PThreads library was used to create and control real-time threads. POSIX semaphores were used to signal between the Scheduler Service and the Capture service while POSIX message queues where used for passing information between Capture Service, PPM/JPEG Service, and Server Service. The Standard Library open, read, write, and close were used for writing files to the file system and writing the file to a socket in cases where are socket is used. Logging could log to either standard out or the system log.

Figures 1: Block Diagrams indicating simple flow, Figure 2. Control Flow and Data Flow Diagram
  inter-service communications, and signaling.	Client Service runs on separate system.
The build system relies on make and produces both the exercise6client.out and exercise6server.out when make is invoked. The server binary executes the image capture while the client binary connects to the server and receives the images the server produces. The build system has multiple build flags that can be invoked when building:

COLOR_LOGS=true, Turn on colored logs (cannot be used with SYS_LOG).
SYS_LOG=true, Log to system log (cannot be used with COLOR_LOGS).
LOG_LEVEL=[0 1 2 3], Turn on minimum log level displayed (used to reduce the output to	standard out).
TYPE=release, Turn on 03 optimization and turn off debug symbols.
NO_COMP=true, Use PPM file format instead of JPEG.

Figure 3. Flow Diagram Scheduler Service Figure 4. Flow Chart Capture Service

The system has 3 or 4 services depending on whether or not NO_COMP is used. The 3 services that are always present are Scheduler Service, Capture Service, and PPM/JPEG Service. The Scheduler Service is very simple. The Scheduler Service signals the Capture Service to capture every period. The Capture Service then signals back to the Scheduler service indicating it is done, and the Scheduler Service gets a time stamp indicating how long the Capture Service took. The Capture Service captures the raw image and passes that data on to the PPM/JPEG service and displays the image to the screen. When the PPM/JPEG Service receives the raw image data it transforms the data into either a PPM file or a JPEG file and writes the contents to disk. If the number of frames captured becomes greater than 2000, the PPM/JPEG Service unlinks the oldest file. When the JPEG service is used, the properly formatted file and the file name are passed on to the Server Service. The Server Service then distributes the file name and file contents over a TCP socket if a client has connected.

Figure 5. Flow Chart PPM Service	Figure 6. Flow Chart JPEG Service

Figure 7. Flow Chart Service (only available with JPEG Service)

Real-Time Analysis and Design:

U = sum ( Ci over Ti ) < m(2^(1/m) -1) = .7798 sub ( 3 services ), .7568 sub(4 services)

Analysis was run on all Minimum, Target, and Stretch requirement scenarios. The Minimum requirement scenario has the most margin of safety. Of the 1000 milliseconds (1 second) for the period only ~78 milliseconds are used. This leaves a safety margin of 92.2% which is clearly greater than the 22.02% required by RM LUB for 3 services. The Target requirements add a couple more milliseconds of execution time but are still within 24.32% required by RM LUB for 4 services. Only 92 of the 1000 milliseconds are used leaving a safety margin of 90.8%. Finally, the Stretch requirements scenario is where scheduling becomes interesting. The period for all services is reduced to 100 milliseconds. As stated in the Target scenario 92 milliseconds are required to complete all services, and this leaves only 8% safety margin which is less than the 24.32% for RM LUB. However, all periods are 100 milliseconds which makes them harmonic. The services are able to be scheduled within the 100 millisecond period and are harmonic which means they can be scheduled for all time. The Cheddar Simulations verify that all services sets are able to be scheduled. Scheduling Point and Completion Time feasibility tests were completed using the source from the RTECS book.

Figure 8: Minimum Requirements Cheddar Simulation 78 of 1000 ms are occupied (Capacity measured in milliseconds and would extend to 1000).

Figure 9. Hand drawn timing diagram for Minimum Requirements.

Figure 10: Target Requirements Cheddar Simulation 92 of 1000 ms are occupied (Capacity measured in milliseconds and would extend to 1000).

Figure 11. Hand drawing timing diagram for Target Requiements.

Figure 12. Target Requirements Cheddar Simulation 92 of 100 ms are occupied (Capacity measured in milliseconds and would extend to 100).

Figure 13. Hand drawn timing diagram for Stretch Requirements.

The results from the system were unexpected. Initially during the proof of concept, the system could not provide predictable results even at the 1 Hz frame rate. After doing some research I realized the frequency scaling was moving around quite a bit during execution. I turned the “ondemand” frequency scaling off and turned on the “performance” setting. This set the system to a steady 2.13 GHz frequency instead of moving between 51 MHz and 2.13 GHz. This helped improve the predictability. To analyze the results the timestamps were grabbed from each image and placed in a spreadsheet. The following are summaries of the results with the full spreadsheet included in the compressed file provided.

Figure 14. Minimum Requirements period and Figure 15. Target Requirements period and jitter
        jitter statistics. statistics.

Figure 16. Stretch Requirements period and jitter
statistics.

It can be seen in the cases for Minimum and Target requirements the system is fairly predictable. Both cases have a time stamp standard deviation of 41 microseconds. The issue I believe is concerning is the -9 milliseconds of accumulated jitter in each case. This may be overcome by adjusting the period so the average is closer to 1 second. However, the average period in both cases is
.999995 seconds and -9 milliseconds over 1800 frames equates to an average of 5 microseconds per frame. The Stretch requirements case looks worse than the Minimum and Target with a period standard deviation of 109 microseconds, but the average looks really good at 100.003 milliseconds. The accumulated jitter is 18.34 milliseconds over 6000 frames coming out to approximately 3 microseconds average which is better than the Minimum and Target requirements. The maximum over-run for the Stretch case is the worse with an over-run of 1.2 milliseconds. Overall I believe the system is very predictable.

Completion Time Feasibility Minimum Requirements / i=0, an=1 / an=1, deadline[0]=1000 / i=1, an=71 / an=71, deadline[1]=1000 / i=2, an=78 / an=78, deadline[2]=1000 / FEASIBLE	Scheduling Point Feasibility Minimum Requirements / temp: 1, val: 1000 / temp: 71, val: 1000 / temp: 78, val: 1000 / FEASIBLE
Completion Time Feasibility Target Requirements / i=0, an=1 / an=1, deadline[0]=1000 / i=1, an=71 / an=71, deadline[1]=1000 / i=2, an=91 / an=91, deadline[2]=1000 / i=3, an=92 / an=92, deadline[3]=1000 / FEASIBLE	Scheduling Point Feasibility Target Requirements / temp: 1, val: 1000 / temp: 71, val: 1000 / temp: 91, val: 1000 / temp: 92, val: 1000 / FEASIBLE
Completion Time Feasibility Stretch Requirements / i=0, an=1 / an=1, deadline[0]=100 / i=1, an=71 / an=71, deadline[1]=100 / i=2, an=91 / an=91, deadline[2]=100 / i=3, an=92 / an=92, deadline[3]=100 / FEASIBLE	Scheduling Point Feasibility Stretch Requirements / temp: 1, val: 100 / temp: 71, val: 100 / temp: 91, val: 100 / temp: 92, val: 100 / FEASIBLE

Table 1. Scheduling Point and Completion Time feasibility test results (All FEASIBLE).

To be safe the the WCET was calculated by taking an average of the execution times and doubling it. During execution of the 3 test cases the execution times stayed around the average execution time providing even more margin of safety than expected. Another interesting item I noticed was the Capture Service response time was significantly less than the average that was generated during testing. The averages were calculated with each service running without any of the other services running. The Capture Service was IO bound by the frame rate of the camera having an average execution time close to 33.3333 milliseconds. When all services ran together, time that would have been spent waiting for the next frame to be ready was occupied by the other services. This fact allowed the system to be run at the max frame rate. The analysis was not included in this document because it was not a requirement, but the full analysis spread sheet was included in the compressed file.

Proof of Concept and Tests:

The Minimum Requirements test required that 1800 PPM frames be captured at 1 FPS. The following two shots are the first and last frame from the capture.

        Figure 17. First Shot of Capture Figure 18. Last Shot of Capture.

The following is an example of the header that is in the PPM in a hex dump format which shows the time stmap and the uname information:

00000000: 5036 0a36 3430 2034 3830 0a23 2054 696d P6.640 480.# Tim
00000010: 6573 7461 6d70 3a20 3135 3032 3035 3730 estamp: 15020570
00000020: 3235 2e30 3632 3130 390a 2320 756e 616d 25.062109.# unam
00000030: 653a 204c 696e 7578 2074 6567 7261 2d75 e: Linux tegra-u
00000040: 6275 6e74 7520 332e 3130 2e34 3020 2331 buntu 3.10.40 #1
00000050: 2053 4d50 2050 5245 454d 5054 2053 756e SMP PREEMPT Sun
00000060: 204a 756c 2033 3020 3030 3a31 333a 3130 Jul 30 00:13:10
00000070: 2055 5443 2032 3031 3720 6172 6d76 376c UTC 2017 armv7l
00000080: 0a32 3535 0aec f1ff ecf1 fff2 f0f3 f2f0 .255...........

        Figure 19: First Image of the Capture Figure 20: Last Image of the Capture.

The Stretch Requirements test required that 6000 JPEG frames be captured at 10 FPS. The following two shots are the first and last frame from the capture.

   Figure 21: First Image of Stretch Requirements. Figure 22: Last Image of Stretch Requirements.

Shown in the images there is a discrepancy in the beginning and end time (~4 seconds). Looking through the images they start displaying 100 ms periodicity in the image (the time stamp always has a 100 ms periodicity) around the 4th or 5th capture. At the beginning of each test run the system captures 10 images and displays them to the screen that are not part of the capture to warm up the camera. I assume these images were still in a buffer and the call to get the image returned stale data from the buffer.

The following is an example of the header that is in the JPEG in a hex dump format which shows the time stamp and the uname information:

00000000: ffd8 fffe 0079 2320 5469 6d65 7374 616d .....y# Timestam
00000010: 703a 2031 3530 3230 3535 3030 302e 3939 p: 1502055000.99
00000020: 3038 3732 0a00 2320 756e 616d 653a 204c 0872..# uname: L
00000030: 696e 7578 2074 6567 7261 2d75 6275 6e74 inux tegra-ubunt
00000040: 7520 332e 3130 2e34 3020 2331 2053 4d50 u 3.10.40 #1 SMP
00000050: 2050 5245 454d 5054 2053 756e 204a 756c PREEMPT Sun Jul
00000060: 2033 3020 3030 3a31 333a 3130 2055 5443 30 00:13:10 UTC
00000070: 2032 3031 3720 6172 6d76 376c 0aff e000 2017 armv7l....

This project was fun and challenging. Getting predictable results was surprising after being warned about the short comings of Linux in the Real-Time context. Being able to run the system at the maximum frame rate of the camera under good conditions was also very surprising. I plan on testing this system on platforms with fewer resources, BeagleBoneBlack and Raspberry Pi, to see how well it performs under those conditions.

Appendix:

Files:
Directories in the ZIP file contain these files:
analysis: All of the statistical analysis spreadsheets.
minimum: All of the images for the Minimum Requirements.
target: All of the images for the Target Requirements.
stretch: All of the images for the Stretch Requirements.
max_frame_rate: All of the images for the Max Frame Rate test.
videos: All of the videos that were compiled from the images.

Source:

/** @file ppm.c
*
* @brief Holds NetPBM PPM specific code
*
*/

#include <errno.h>
#include <math.h>
#include <mqueue.h>
#include <pthread.h>
#include <stdint.h>
#include <stdlib.h>
#include <string.h>
#include <time.h>
#include <unistd.h>

#include "capture.h"
#include "log.h"
#include "project_defs.h"
#include "profiler.h"
#include "ppm.h"
#include "utilities.h"

// File storage info
#define FILE_NAME_MAX (255)
#define UNAME_MAX (255)
#define DIR_NAME "capture_ppm"
#define FILE_NAME_FMT "%s/capture_%04d.ppm"

// Image info
#define MAX_INTENSITY_STR "255\n"
#define MAX_INTENSITY_STR_LEN (4)
#define P6_HEADER "P6\n640 480\n"
#define P6_HEADER_LEN (11)
#define MAX_INTENSITY (255)
#define MAX_INTENSITY_FLOAT (255.0f)

// Image buffer for current frame used to hold converted PPM file
static char image_buf[IMAGE_NUM_BYTES];

// Abort flag
extern uint8_t abort_test;

// PPM capture info
typedef struct {
  // Hold the uname str
  char uname_str[UNAME_MAX];

  // Length of uname string
  uint8_t uname_len;

  // Resolution info
  resolution_t resolution;

  // Timestamp to place in image
  char timestamp[TIMESTAMP_MAX];

  // Captupre info object
  cap_info_t cap;

  // Filename
  char file_name[FILE_NAME_MAX];
} ppm_cap_t;

/*!
* @brief Applies gamma transfer function to color intensity
* @param color color intensity
* @return transformed result
*/
static inline
uint8_t gamma_tf(uint8_t color)
{
  FUNC_ENTRY;
  float conversion = (float)color / MAX_INTENSITY_FLOAT;
  if (conversion >= 0 && conversion < 0.0013f)
  {
    return (uint8_t) ((float)(12.92f * conversion) * MAX_INTENSITY);
  }
  else
  {
    return (uint8_t) ((float)(1.055f * pow(conversion, .4545f) - 0.055f) * MAX_INTENSITY);
  }
} // gamma_tf()

/*!
* @brief Writes ppm to file and socket
* @param fd file descriptor to write ppm to
* @param ppm struct holding ppm data to write to fd
* @return SUCCESS/FAILURE
*/
static inline
uint32_t write_ppm(uint32_t fd, ppm_cap_t * ppm)
{
  FUNC_ENTRY;
  CHECK_NULL(ppm);

  int32_t res = 0;

  LOG_LOW("Writing ppm image to fd: %d", fd);
  // Write the header
  EQ_RET_E(res,
        write(fd, (void *) P6_HEADER, P6_HEADER_LEN),
        -1,
        FAILURE);

  // Write the timestamp comment
  EQ_RET_E(res,
        write(fd, (void *) ppm->timestamp, strlen(ppm->timestamp)),
        -1,
        FAILURE);

  // Write the uname string comment
  EQ_RET_E(res,
        write(fd, (void *) ppm->uname_str, ppm->uname_len),
        -1,
        FAILURE);

  // Write the max val
  EQ_RET_E(res,
        write(fd, (void *) MAX_INTENSITY_STR, MAX_INTENSITY_STR_LEN),
        -1,
        FAILURE);

  // Write the color data
  EQ_RET_E(res, write(fd, (void *)image_buf, IMAGE_NUM_BYTES), -1, FAILURE);

  // Success
  return SUCCESS;
} // write_ppm()

/*!
* @brief Puts image buffer rgb in correct format
* @param ppm ppm structure to set data pointer
* @param data imageData casted as a colors_t data structure
* @return SUCCESS/FAILURE
*/
static inline
uint32_t create_image_buf(ppm_cap_t * ppm, colors_t * data)
{
  FUNC_ENTRY;
  CHECK_NULL(data);
  CHECK_NULL(ppm);

  uint32_t count = 0;

  // Write the image buffer with proper info
  for (uint32_t vres = 0; vres < ppm->resolution.vres; vres++)
  {
    for (uint32_t hres = 0; hres < ppm->resolution.hres; hres++)
    {
#ifdef GAMMA_FUNCTION
      // Do gamma function conversion which is specified by the NetPbm spec
      image_buf[count] = gamma_tf(data->green);
      image_buf[count + 1] = gamma_tf(data->blue);
      image_buf[count + 2] = gamma_tf(data->red);
#else // GAMMA_FUNCTION
      // Write the raw intensity
      image_buf[count] = (data->red);
      image_buf[count + 1] = (data->green);
      image_buf[count + 2] = (data->blue);
#endif // GAMMA_FUNCTION
      count += 3;
      data++;
    }
  }

  // Set the color data pointer to image buf
  return SUCCESS;
} // create_image_buf()

/*!
* @brief Handles inccming messages from queue
* @param no information passed
* @return NULL
*/
void * ppm_service(void * param)
{
  FUNC_ENTRY;
  struct timespec diff;
  ppm_cap_t cap;
  int32_t res = 0;
  uint32_t fd = 0;
  uint32_t count = 0;
  uint8_t timer = profiler_init();
  char unlink_name[FILE_NAME_MAX];
  image_q_inf_t image_q_inf;

  // Set the resolution
  cap.resolution.hres = HRES;
  cap.resolution.vres = VRES;

  // Try to create the queue
  EQ_RET_EA(image_q_inf.image_q,
        mq_open(QUEUE_NAME, O_RDONLY | O_CREAT, S_IRWXU, NULL),
        -1,
        NULL,
        abort_test);

  // Get the message queue attributes
  NOT_EQ_RET_EA(res,
        mq_getattr(image_q_inf.image_q, &image_q_inf.attr),
        SUCCESS,
        NULL,
        abort_test)

  // Get the uname string and display
  EQ_RET_EA(res, get_uname(cap.uname_str, UNAME_MAX), FAILURE, NULL, abort_test);
  LOG_LOW("Using uname string: %s", cap.uname_str);
  cap.uname_len = strlen(cap.uname_str);

  while(!abort_test)
  {
    // Get the time after the loop is done
    GET_TIME;

    // Display the timestamp
    DISPLAY_TIMESTAMP;

    // Create the file name to save data
    snprintf(cap.file_name, FILE_NAME_MAX, FILE_NAME_FMT, DIR_NAME, count);
    LOG_LOW("Using %s file name", cap.file_name);
    EQ_RET_EA(res,
        mq_receive(image_q_inf.image_q, (char *)&cap.cap, image_q_inf.attr.mq_msgsize, NULL),
        -1,
        NULL,
        abort_test);

    // Start the timer after the message has been capture to write to disk
    START_TIME;

    // Translate the data from the capture buffer into properly formatted ppm
    // data
    NOT_EQ_RET_EA(res,
        create_image_buf(&cap, (colors_t *)cap.cap.frame->imageData),
        SUCCESS,
        NULL,
        abort_test);

    // Open file to store contents
    EQ_RET_EA(fd,
        open(cap.file_name, O_CREAT | O_WRONLY, FILE_PERM),
        -1,
        NULL,
        abort_test);

    // Add the timestamp to the image comment
    EQ_RET_EA(res,
        get_timestamp(&cap.cap.time, cap.timestamp, TIMESTAMP_MAX),
        FAILURE,
        NULL,
        abort_test);

    // Write data to file
    NOT_EQ_RET_EA(res, write_ppm(fd, &cap), SUCCESS, NULL, abort_test);

    // Close file properly
    EQ_RET_EA(res, close(fd), -1, NULL, abort_test);

    // Unlink old file if the number for frames is greater than the max frame setting
    res = count - MAX_FRAMES;
    if (res > -1)
    {
      snprintf(unlink_name, FILE_NAME_MAX, FILE_NAME_FMT, DIR_NAME, res);
      LOG_LOW("Unlinking %s", unlink_name);
      EQ_RET_EA(res, unlink(unlink_name), -1, NULL, abort_test);
    }

    // Increment counter
    count++;
  }
  LOG_HIGH("ppm_service thread exiting");
  mq_close(image_q_inf.image_q);
  return NULL;
} // ppm_service()

uint32_t ppm_init()
{
  FUNC_ENTRY;
  struct sched_param sched;
  struct sched_param ppm_sched;
  pthread_attr_t sched_attr;
  pthread_t ppm_thread;
  int32_t res = 0;
  int32_t rt_max_pri = 0;
  int32_t ppm_policy = 0;

  // Try to create directory for storing images
  EQ_RET_E(res, create_dir(DIR_NAME), FAILURE, FAILURE);

  // Initialize the schedule attributes
  PT_NOT_EQ_EXIT(res, pthread_attr_init(&sched_attr), SUCCESS);

  // Set the attributes structure to PTHREAD_EXPLICIT_SCHED and SCHED_FIFO
  PT_NOT_EQ_RET(res,
        pthread_attr_setinheritsched(&sched_attr, PTHREAD_EXPLICIT_SCHED),
        SUCCESS,
        FAILURE);
  PT_NOT_EQ_RET(res,
        pthread_attr_setschedpolicy(&sched_attr, SCHED_FIFO),
        SUCCESS,
        FAILURE);

  // Get the max priority
  EQ_RET_E(rt_max_pri, sched_get_priority_max(SCHED_FIFO), -1, FAILURE);

  // Set the priority to max - 1 for the test thread
  sched.sched_priority = rt_max_pri - 1;
  PT_NOT_EQ_RET(res,
        pthread_attr_setschedparam(&sched_attr, &sched),
        SUCCESS,
        FAILURE);
  // Create pthread
  PT_NOT_EQ_RET(res,
        pthread_create(&ppm_thread, &sched_attr, ppm_service, NULL),
        SUCCESS,
        FAILURE);

  // Get the scheduler parameters to display
  PT_NOT_EQ_RET(res,
        pthread_getschedparam(ppm_thread, &ppm_policy, &ppm_sched),
        SUCCESS,
        FAILURE);
  LOG_HIGH("ppm_service policy: %d, priority: %d",
        ppm_policy,
        ppm_sched.sched_priority);
  return SUCCESS;
} // ppm_init()

/** @file log.c
*
* @brief Holds functions used for logging
*
*/

#if defined(SYS_LOG) && defined(COLOR_LOGS)
  #error "Color logs not allowed in system log"
#endif

#include <pthread.h>
#include <stdint.h>
#include <stdio.h>
#include <string.h>
#include <stdarg.h>
#include <syslog.h>

#include "log.h"
#include "project_defs.h"

// TODO: Make this work on both Linux and Windows for cross compilation
#define PATH_SEPARATOR "/"
#define LOG_BUFFER_MAX (1024)
#define STRNCAT_MAX (LOG_BUFFER_MAX - 1)

// String log levels
static const char * p_log_level_str[] = {
  "HIGH",
  "MEDIUM",
  "LOW",
  "ERROR",
  "FATAL"
};

#ifdef COLOR_LOGS
// String log level colors
static const char * p_log_color_str[] = {
  "\e[1;96m", // High=CYAN
  "\e[1;93m", // Medium=YELLOW
  "\e[1;97m", // Low=WHITE
  "\e[1;91m", // Error=RED
  "\e[1;95m", // Fatal=PURPLE
};

// Format for color
#define LOG_COLOR_FMT "%s%-7s %-11s in [%20s] line %4u: "

#else
// Format for non-color logs
#define LOG_FMT "%-7s %-11s in [%20s] line %4u: "

#endif /* COLOR_LOGS */

/*!
* @brief Get the file basename in a OS that uses "/" for the separator
* @param[in] p_filename pointer to the file name
* @param[in] p_path_separator pointer to the path separator
* @return pointer to the basename
*/
static inline char * get_basename(char * p_filename, const char * p_path_seperator)
{
  uint8_t found_last_occurence = 0;

  // Loop of string looking for instances of p_path_separator until
  // the last instance is found. Use that as basename.
  while (!found_last_occurence)
  {
    char * p_temp = strstr(p_filename, p_path_seperator);
    if (p_temp != NULL)
    {
      p_filename = p_temp + 1;
    }
    else
    {
      found_last_occurence = 1;
    }
  }

  // Return a pointer to the file name
  return p_filename;
} // get_basename()

void log_init()
{
#ifdef SYS_LOG
  openlog("ecen5623", LOG_CONS | LOG_PID, LOG_USER);
#endif
} // log_init()

void log_destroy()
{
#ifdef SYS_LOG
  closelog();
#endif
} // log_destroy()

void log_level
(
  log_level_t level,
  char * p_filename,
  const char * p_function,
  uint32_t line_no,
  ...
)
{
  va_list printf_args;
  char * fmt;
  char log_buffer[LOG_BUFFER_MAX];
  char fmt_buffer[LOG_BUFFER_MAX];

  // Point to the last argument where the variadic arguments start
  va_start(printf_args, line_no);

  // Get the first argument which will be the format for the printf statement
  fmt = va_arg(printf_args, char *);

#ifdef COLOR_LOGS
  // Print header in color
  snprintf(log_buffer,
        LOG_BUFFER_MAX,
        LOG_COLOR_FMT,
        p_log_color_str[level],
        p_log_level_str[level],
        get_basename(p_filename, PATH_SEPARATOR),
        p_function,
        line_no);
#else
  // Print the header without color
  snprintf(log_buffer,
        LOG_BUFFER_MAX,
        LOG_FMT,
        p_log_level_str[level],
        get_basename(p_filename, PATH_SEPARATOR),
        p_function,
        line_no);

#endif /* COLOR_LOGS */
  // Print the statement provided in the ... variadic parameter
  vsnprintf(fmt_buffer, LOG_BUFFER_MAX, fmt, printf_args);
  strncat(log_buffer, fmt_buffer, STRNCAT_MAX);

#ifdef COLOR_LOGS
  // Print the ending color and newline
  strncat(log_buffer, "\e[0m\n", STRNCAT_MAX);
#else
  //printf("\n");
  strncat(log_buffer, "\n", STRNCAT_MAX);
#endif /* COLOR_LOGS */
  va_end(printf_args);

#ifdef SYS_LOG
  // Log to syslog
  syslog(LOG_INFO, "%s", log_buffer);
#else
  // Print the generated string
  printf("%s", log_buffer);
#endif // SYSLOG

} // log_level()

/** @file profiler.c
*
* @brief Function definitions for profiler
*
*/

#include <time.h>
#include <stdint.h>
#include <stdlib.h>

#include "profiler.h"
#include "log.h"

struct timespec start[256];
struct timespec end[256];
uint8_t num_timers = 0;

#define NSEC_PER_SEC (1000000000)

uint8_t profiler_init()
{
  num_timers++;
  reset_timer(num_timers);
  return num_timers;
} // profiler_init()

int8_t start_timer(uint8_t timer)
{
  return clock_gettime(CLOCK_MONOTONIC, &start[timer]);
} // start_timer()

int8_t stop_timer(uint8_t timer)
{
  return clock_gettime(CLOCK_MONOTONIC, &end[timer]);
} // stop_timer()

void reset_timer(uint8_t timer)
{
  start[timer].tv_nsec = end[timer].tv_nsec = 0;
} // reset_timer()

void get_time(uint8_t timer, struct timespec * diff)
{
  diff->tv_nsec = end[timer].tv_nsec - start[timer].tv_nsec;
  diff->tv_sec = end[timer].tv_sec - start[timer].tv_sec;

  if (diff->tv_nsec < 0)
  {
    diff->tv_sec -= 1;
    diff->tv_nsec += NSEC_PER_SEC;
  }
} // get_time()

/** @file jpeg.c
*
* @brief Holds JPEG specific code
*
*/

#include <errno.h>
#include <math.h>
#include <mqueue.h>
#include <pthread.h>
#include <stdint.h>
#include <stdlib.h>
#include <string.h>
#include <time.h>
#include <unistd.h>

#include "capture.h"
#include "jpeg.h"
#include "log.h"
#include "project_defs.h"
#include "profiler.h"
#include "server.h"
#include "utilities.h"

// File storage info
#define UNAME_MAX (255)
#define IMAGE_EXT ".jpeg"
#define FILE_NAME_FMT "%s/capture_%04d.jpeg"
#define NUM_IMAGE_BUFS (4)

// Flag for setting abort status
extern uint8_t abort_test;

// Server accepting images to send

// Location to store JPEG data and pass to TCP client service. Using multiple buffering
// for safety of data without using MUTEX.
static uint8_t image_buf[NUM_IMAGE_BUFS][IMAGE_NUM_BYTES];

// Struct of information for the thread
typedef struct {
  // Image buffer for current frame
  uint8_t * cur_buf;

  // Hold the uname str
  char uname_str[UNAME_MAX];
  uint16_t uname_len;
  uint16_t comment_len;

  // Filename
  char file_name[FILE_NAME_MAX];

  // Current image pointer
  CvMat * image;

  // Capture info object
  cap_info_t cap;
} jpeg_cap_t;

// Add data macro
#define ADD_DATA(dest, src, count, tally) memcpy(&dest[tally], src, count); tally += count

/*!
* @brief Builds the JPEG file buffer and writes to file
* @param cap current capture information
* @return SUCCESS/FAILURE
*/
static inline
uint32_t write_jpeg(jpeg_cap_t * cap)
{
  FUNC_ENTRY;
  int32_t res = 0;
  int32_t fd = 0;
  uint32_t cur_loc = 0;
  char timestamp[TIMESTAMP_MAX];
  char image_start[] = {0xff, 0xd8};
  char com_start[] = {0xff, 0xfe};

  // Open file to store contents
  EQ_RET_E(fd, open(cap->file_name, O_CREAT | O_RDWR, FILE_PERM), -1, FAILURE);

  // Add the timestamp to the image comment
  EQ_RET_E(res,
        get_timestamp(&cap->cap.time, timestamp, TIMESTAMP_MAX),
        FAILURE,
        FAILURE);

  // Add all image data to a buffer including header
  ADD_DATA(cap->cur_buf, image_start, 2, cur_loc);
  ADD_DATA(cap->cur_buf, com_start, 2, cur_loc);
  ADD_DATA(cap->cur_buf, &(cap->comment_len), 2, cur_loc);
  ADD_DATA(cap->cur_buf, timestamp, TIMESTAMP_MAX, cur_loc);
  ADD_DATA(cap->cur_buf, cap->uname_str, cap->uname_len, cur_loc);
  ADD_DATA(cap->cur_buf, (cap->image->data.ptr + 2), cap->image->cols, cur_loc);

  // Write the file out
  EQ_RET_E(res, write(fd, cap->cur_buf, cur_loc), -1, FAILURE);

  // Close file properly
  EQ_RET_E(res, close(fd), -1, FAILURE);

  return cur_loc;
}

/*!
* @brief Handles incoming messages from queue
* @param param no information is passed
* @return NULL
*/
void * jpeg_service(void * param)
{
  FUNC_ENTRY;
  struct timespec diff;
  image_q_inf_t image_q_inf;
  jpeg_cap_t cap;
  mqd_t server_queue;
  server_info_t server_msg;
  const int32_t comp[2] = {CV_IMWRITE_JPEG_QUALITY, 50};
  int32_t res = 0;
  uint32_t count = 0;
  uint8_t timer = profiler_init();
  char unlink_name[FILE_NAME_MAX];

  // Get the uname string and display
  EQ_RET_EA(res, get_uname(cap.uname_str, UNAME_MAX), FAILURE, NULL, abort_test);
  LOG_LOW("Using uname string: %s", cap.uname_str);

  // Get the uname length for the comment
  cap.uname_len = strlen(cap.uname_str);

  // Calculate the total comment length for this image add 2 to include null
  // term
  cap.comment_len = TIMESTAMP_MAX + cap.uname_len + 2;
  cap.comment_len = (cap.comment_len << 8 | cap.comment_len >> 8);

  // Try to create the queue
  EQ_RET_EA(image_q_inf.image_q,
        mq_open(QUEUE_NAME, O_RDONLY | O_CREAT, S_IRWXU, NULL),
        -1,
        NULL,
        abort_test);

  // Try to create the queue
  EQ_RET_E(server_queue,
        mq_open(SERVER_QUEUE_NAME, O_NONBLOCK | O_WRONLY | O_CREAT, S_IRWXU, NULL),
        -1,
        NULL);

  // Get the message queue attributes
  NOT_EQ_RET_EA(res,
        mq_getattr(image_q_inf.image_q, &image_q_inf.attr),
        SUCCESS,
        NULL,
        abort_test)

  while(!abort_test)
  {
    // Get the current buffer from the multi buffer for processing image
    cap.cur_buf = image_buf[count % NUM_IMAGE_BUFS];

    // Get the time after the loop is done
    GET_TIME;

    // Display the timestamp
    DISPLAY_TIMESTAMP;

    // Create the file name to save data
    snprintf(cap.file_name, FILE_NAME_MAX, FILE_NAME_FMT, DIR_NAME, count);
    LOG_LOW("Using %s file name", cap.file_name);
    server_msg.file_name_len = strlen(cap.file_name);
    memcpy(server_msg.file_name, cap.file_name, server_msg.file_name_len);
    EQ_RET_EA(res,
        mq_receive(image_q_inf.image_q, (char *)&cap.cap, image_q_inf.attr.mq_msgsize, NULL),
        -1,
        NULL,
        abort_test);

    // Start the timer for encoding/writing the image
    START_TIME;

    // Encode the frame into JPEG
    EQ_RET_EA(cap.image,
        cvEncodeImage(IMAGE_EXT, cap.cap.frame, comp),
        NULL,
        NULL,
        abort_test);

    // Add comment information
    EQ_RET_EA(res, write_jpeg(&cap), 1, NULL, abort_test);

    server_msg.image_buf_len = res;
    server_msg.image_buf = cap.cur_buf;

    // Try to send the cap info via messaqe queue
    mq_send(server_queue, (char *)&server_msg, sizeof(server_msg), 0),

    // Unlink old file if the number for frames is greater than the max frame setting
    res = count - MAX_FRAMES;
    if (res > -1)
    {
      snprintf(unlink_name, FILE_NAME_MAX, FILE_NAME_FMT, DIR_NAME, res);
      LOG_LOW("Unlinking %s", unlink_name);
      EQ_RET_EA(res, unlink(unlink_name), -1, NULL, abort_test);
    }

    // Increment counter
    count++;
  }
  LOG_HIGH("jpeg_service thread exiting");
  mq_close(image_q_inf.image_q);
  mq_close(server_queue);
  return NULL;
} // jpeg_service()

uint32_t jpeg_init()
{
  FUNC_ENTRY;
  struct sched_param sched;
  struct sched_param jpeg_sched;
  pthread_attr_t sched_attr;
  pthread_t jpeg_thread;
  int32_t res = 0;
  int32_t rt_max_pri = 0;
  int32_t jpeg_policy = 0;

  // Try to create directory for storing images
  EQ_RET_E(res, create_dir(DIR_NAME), FAILURE, FAILURE);

  // Initialize the schedule attributes
  PT_NOT_EQ_EXIT(res, pthread_attr_init(&sched_attr), SUCCESS);

  // Set the attributes structure to PTHREAD_EXPLICIT_SCHED and SCHED_FIFO
  PT_NOT_EQ_RET(res,
        pthread_attr_setinheritsched(&sched_attr, PTHREAD_EXPLICIT_SCHED),
        SUCCESS,
        FAILURE);
  PT_NOT_EQ_RET(res,
        pthread_attr_setschedpolicy(&sched_attr, SCHED_FIFO),
        SUCCESS,
        FAILURE);

  // Get the max priority
  EQ_RET_E(rt_max_pri, sched_get_priority_max(SCHED_FIFO), -1, FAILURE);

  // Set the priority to max - 1 for the test thread
  sched.sched_priority = rt_max_pri - 1;
  PT_NOT_EQ_RET(res,
        pthread_attr_setschedparam(&sched_attr, &sched),
        SUCCESS,
        FAILURE);
  // Create pthread
  PT_NOT_EQ_RET(res,
        pthread_create(&jpeg_thread, &sched_attr, jpeg_service, NULL),
        SUCCESS,
        FAILURE);

  // Get the scheduler parameters to display
  PT_NOT_EQ_RET(res,
        pthread_getschedparam(jpeg_thread, &jpeg_policy, &jpeg_sched),
        SUCCESS,
        FAILURE);
  LOG_HIGH("jpeg_service policy: %d, priority: %d",
        jpeg_policy,
        jpeg_sched.sched_priority);
  return SUCCESS;
} // jpeg_init()

/** @file client_main.c
*
* @brief Main for client
*
*/

#include <stdint.h>
#include <client.h>

int main()
{
  return client_init();
}

/** @file client.c
*
* @brief Holds functionality for socket client
*
*/

#include <errno.h>
#include <mqueue.h>
#include <netinet/in.h>
#include <netdb.h>
#include <pthread.h>
#include <semaphore.h>
#include <stdint.h>
#include <stdlib.h>
#include <string.h>
#include <time.h>
#include <sys/socket.h>
#include <unistd.h>

#include "client.h"
#include "jpeg.h"
#include "log.h"
#include "project_defs.h"
#include "server.h"
#include "utilities.h"

#define SERVER_PORT (12345)
#define ADDRESS "10.0.0.29"

// Inform the main that service is done
static sem_t done;

/*!
* @brief Ensure to receive all bytes on a read
* @param sockfd socket file descriptor
* @param data location to store data
* @param count number of bytes to read
* @return number of bytes read
*/
static inline
uint32_t client_recv(int32_t sockfd, void * data, uint32_t count)
{
  FUNC_ENTRY;

  int32_t bytes = 0;
  int32_t res = 0;

  while (bytes < count)
  {
    EQ_RET_E(res, read(sockfd, data + bytes, count - bytes), -1, -1);
    bytes += res;
  }
  return bytes;
} // client_recv()

/*!
* @brief Shutdown socked
* @param sockfd socket file descriptor
* @return SUCCESS/FAILURE
*/
uint32_t client_dest(int32_t sockfd)
{
  FUNC_ENTRY;

  int32_t res = 0;

  // Shutdown the socket
  LOG_MED("Shutting down socket fd: %d", sockfd);
  EQ_RET_E(res, shutdown(sockfd, SHUT_RDWR), -1, FAILURE);

  return SUCCESS;
} // client_dest()

/*!
* @brief Handles incoming messages on queue
* @param param no data
* @return NULL
*/
void * client_service(void * param)
{
  FUNC_ENTRY;

  struct hostent * server;
  struct sockaddr_in serv_addr;
  int32_t res = 0;
  int32_t sockfd;
  int32_t name_len = 0;
  int32_t buf_len = 0;
  int32_t fd = 0;
  char file_name[FILE_NAME_MAX];
  uint8_t image_buf[IMAGE_NUM_BYTES];

  // Memset the serv_addr struct to 0
  memset((void *)&serv_addr, 0, sizeof(serv_addr));

  // Instantiate socket and get the host name for connection
  EQ_RET_E(sockfd, socket(AF_INET, SOCK_STREAM, 0), -1, NULL);
  EQ_RET_E(server, gethostbyname(ADDRESS), NULL, NULL);

  // Set up the serv_addr structure for connection
  serv_addr.sin_family = AF_INET;
  memcpy(&serv_addr.sin_addr.s_addr, server->h_addr, server->h_length);
  serv_addr.sin_port = htons(SERVER_PORT);

  // Connect
  LOG_HIGH("Trying connection to %s on port %d", ADDRESS, SERVER_PORT);
  EQ_RET_E(res,
        connect(sockfd, (struct sockaddr *)&serv_addr, sizeof(serv_addr)),
        -1,
        NULL);
  LOG_HIGH("Connection successful");

  // Loop catching the file name size, file name, image buffer size, image buffer
  while(1)
  {
      // Receive the file name
      EQ_RET_E(res, client_recv(sockfd, &name_len, sizeof(name_len)), -1, NULL);
      name_len = htons(name_len);
      if (name_len > FILE_NAME_MAX)
      {
        LOG_ERROR("File name length %d is too long exiting", name_len);
        break;
      }
      EQ_RET_E(res, client_recv(sockfd, file_name, name_len), -1, NULL);
      LOG_LOW("Receiving file name %s", file_name);

      // Receive the buffer
      EQ_RET_E(res, client_recv(sockfd, &buf_len, sizeof(buf_len)), -1, NULL);
      buf_len = htons(buf_len);
      LOG_LOW("Trying to read %d bytes", buf_len);
      EQ_RET_E(res, client_recv(sockfd, image_buf, buf_len), -1, NULL);
      if (buf_len > IMAGE_NUM_BYTES)
      {
        LOG_ERROR("Buffer length %d is too long exiting, buf_len");
        break;
      }
      LOG_HIGH("Received %s", file_name);
      LOG_LOW("Received %d bytes", res);

      // Open file to store contents
      EQ_RET_E(fd, open(file_name, O_CREAT | O_RDWR, FILE_PERM), -1, NULL);
      EQ_RET_E(res, write(fd, image_buf, buf_len), -1, NULL);
      EQ_RET_E(res, close(fd), -1, NULL);
  }
  LOG_HIGH("client_service exiting");
  client_dest(sockfd);
  return NULL;
} // client_service()

uint32_t client_init()
{
  FUNC_ENTRY;
  struct sched_param sched;
  struct sched_param client_sched;
  pthread_attr_t sched_attr;
  pthread_t client_thread;
  int32_t res = 0;
  int32_t rt_max_pri = 0;
  int32_t client_policy = 0;

  // Semaphore for signaling done
  PT_NOT_EQ_EXIT(res, sem_init(&done, 0, 0), SUCCESS);

  // Try to create directory for storing images
  EQ_RET_E(res, create_dir(DIR_NAME), FAILURE, FAILURE);

  // Initialize the schedule attributes
  PT_NOT_EQ_RET(res, pthread_attr_init(&sched_attr), SUCCESS, FAILURE);

  // Set the attributes structure to PTHREAD_EXPLICIT_SCHED and SCHED_FIFO
  PT_NOT_EQ_RET(res,
        pthread_attr_setinheritsched(&sched_attr, PTHREAD_EXPLICIT_SCHED),
        SUCCESS,
        FAILURE);
  PT_NOT_EQ_RET(res,
        pthread_attr_setschedpolicy(&sched_attr, SCHED_FIFO),
        SUCCESS,
        FAILURE);

  // Get the max priority
  EQ_RET_E(rt_max_pri, sched_get_priority_max(SCHED_FIFO), -1, FAILURE);

  // Set the priority to max - 1 for the test thread
  sched.sched_priority = rt_max_pri - 4;
  PT_NOT_EQ_RET(res,
        pthread_attr_setschedparam(&sched_attr, &sched),
        SUCCESS,
        FAILURE);

  // Create pthread
  PT_NOT_EQ_RET(res,
        pthread_create(&client_thread, &sched_attr, client_service, NULL),
        SUCCESS,
        FAILURE);

  // Get the scheduler parameters to display
  PT_NOT_EQ_RET(res,
        pthread_getschedparam(client_thread, &client_policy, &client_sched),
        SUCCESS,
        FAILURE);
  LOG_HIGH("client_service policy: %d, priority: %d",
        client_policy,
        client_sched.sched_priority);

  // Wait for thread to join
  pthread_join(client_thread, NULL);
  return SUCCESS;
} // client_init()

/** @file server.c
*
* @brief Holds functions for a TCP server
*
*/

#include <errno.h>
#include <mqueue.h>
#include <netinet/in.h>
#include <pthread.h>
#include <stdint.h>
#include <stdlib.h>
#include <string.h>
#include <time.h>
#include <sys/socket.h>
#include <unistd.h>

#include "log.h"
#include "project_defs.h"
#include "server.h"

#define SERVER_PORT (12345)
#define SOCKET_BACKLOG_LEN (5)

// Global abort flag
extern uint32_t abort_test;

/*!
* @brief Sends JPEG file over socket to client
* @param param no data
* @return NULL
*/
void * server_service(void * param)
{
  FUNC_ENTRY;

  mqd_t server_queue;
  server_info_t server_msg;
  struct mq_attr attr;
  struct sockaddr_in serv_addr;
  struct sockaddr_in cli_addr;

  int32_t sockfd;
  int32_t newsockfd = 0;
  int32_t res = 0;
  uint32_t clilen;
  uint32_t name_len;
  uint32_t buf_len;

  // Try to create the queue
  EQ_RET_E(server_queue,
        mq_open(SERVER_QUEUE_NAME, O_RDONLY | O_CREAT, S_IRWXU, NULL),
        -1,
        NULL);

  // Get the server queue attributes
  NOT_EQ_RET_EA(res,
        mq_getattr(server_queue, &attr),
        SUCCESS,
        NULL,
        abort_test)

  // Clear out old messages in queue
  LOG_HIGH("Clearing out %d messages", attr.mq_curmsgs);
  for (uint32_t i = 0; i < attr.mq_curmsgs; i++)
  {
    EQ_RET_E(res,
        mq_receive(server_queue, (char *)&server_msg, attr.mq_msgsize, NULL),
        -1,
        NULL);
  }

  // Create a socket file descriptor
  EQ_RET_E(sockfd, socket(AF_INET, SOCK_STREAM, 0), -1, NULL);

  // Initialize server address
  memset((char *) &serv_addr, 0, sizeof(serv_addr));
  serv_addr.sin_family = AF_INET;
  serv_addr.sin_addr.s_addr = INADDR_ANY;
  serv_addr.sin_port = htons(SERVER_PORT);

  // Bind the server socket
  EQ_RET_E(res,
        bind(sockfd, (struct sockaddr *) &serv_addr, sizeof(serv_addr)),
        -1,
        NULL);
  LOG_MED("Bind Successful on port %d", SERVER_PORT);

  // Set the socket as a passive socket
  EQ_RET_E(res, listen(sockfd, SOCKET_BACKLOG_LEN), -1, NULL);
  clilen = sizeof(cli_addr);

  while(!abort_test)
  {
    // Wait for incoming connections
    EQ_RET_E(newsockfd,
        accept(sockfd, (struct sockaddr *)&cli_addr, &clilen),
        -1,
        NULL);

    // Log connection stats
    LOG_MED("Accepted Connection from %d on port %d",
        cli_addr.sin_addr.s_addr,
        cli_addr.sin_port);

    // Loop until read returns 0 bytes
    while(1)
    {

      // Wait for a message with file to send
      EQ_RET_E(res,
        mq_receive(server_queue, (char *)&server_msg, attr.mq_msgsize, NULL),
        -1,
        NULL);

      // Transform to network format
      name_len = htons(server_msg.file_name_len);
      buf_len = htons(server_msg.image_buf_len);

      // Send name length, file name, buffer length, and buffer over socket
      LOG_FATAL("Sending file %s over socket", server_msg.file_name);
      EQ_RET_E(res, write(newsockfd, &name_len, sizeof(name_len)), -1, NULL);
      EQ_RET_E(res,
        write(newsockfd, server_msg.file_name, server_msg.file_name_len),
        -1,
        NULL);
      EQ_RET_E(res, write(newsockfd, &buf_len, sizeof(buf_len)), -1, NULL);
      EQ_RET_E(res,
        write(newsockfd, server_msg.image_buf, server_msg.image_buf_len),
        -1,
        NULL);
    }
  }

  LOG_HIGH("server_service thread exiting");
  mq_close(server_queue);
  close(sockfd);
  if (newsockfd)
  {
    close(newsockfd);
  }
  return NULL;
} // server_service()

uint32_t server_init()
{
  FUNC_ENTRY;
  struct sched_param sched;
  struct sched_param server_sched;
  pthread_attr_t sched_attr;
  pthread_t server_thread;
  int32_t res = 0;
  int32_t rt_max_pri = 0;
  int32_t server_policy = 0;

  // Initialize the schedule attributes
  PT_NOT_EQ_EXIT(res, pthread_attr_init(&sched_attr), SUCCESS);

  // Set the attributes structure to PTHREAD_EXPLICIT_SCHED and SCHED_FIFO
  PT_NOT_EQ_RET(res,
        pthread_attr_setinheritsched(&sched_attr, PTHREAD_EXPLICIT_SCHED),
        SUCCESS,
        FAILURE);
  PT_NOT_EQ_RET(res,
        pthread_attr_setschedpolicy(&sched_attr, SCHED_FIFO),
        SUCCESS,
        FAILURE);

  // Get the max priority
  EQ_RET_E(rt_max_pri, sched_get_priority_max(SCHED_FIFO), -1, FAILURE);

  // Set the priority to max - 1 for the test thread
  sched.sched_priority = rt_max_pri - 1;
  PT_NOT_EQ_RET(res,
        pthread_attr_setschedparam(&sched_attr, &sched),
        SUCCESS,
        FAILURE);
  // Create pthread
  PT_NOT_EQ_RET(res,
        pthread_create(&server_thread, &sched_attr, server_service, NULL),
        SUCCESS,
        FAILURE);

  // Get the scheduler parameters to display
  PT_NOT_EQ_RET(res,
        pthread_getschedparam(server_thread, &server_policy, &server_sched),
        SUCCESS,
        FAILURE);
  LOG_HIGH("server_service policy: %d, priority: %d",
        server_policy,
        server_sched.sched_priority);
  return SUCCESS;
} // server_init()

/** @file server_main.c
*
* @brief Main file for projects
*
*/

#include <stdint.h>
#include <capture.h>

int main()
{
  return sched_service();
}
/** @file template.c
*
* @brief A description of the module’s purpose.
*
*/

#include <errno.h>
#include <stdint.h>
#include <stdio.h>
#include <string.h>
#include <sys/stat.h>
#include <sys/types.h>
#include <sys/utsname.h>
#include <time.h>

#include "log.h"
#include "project_defs.h"
#include "utilities.h"

uint32_t get_uname(char * uname_str, uint32_t count)
{
  FUNC_ENTRY;
  CHECK_NULL(uname_str);
  struct utsname info;
  uint32_t res = 0;

  // Create and write the uname info
  EQ_RET_E(res, uname(&info), -1, FAILURE);
  res = snprintf(uname_str,
        count,
        "# uname: %s %s %s %s %s\n",
        info.sysname,
        info.nodename,
        info.release,
        info.version,
        info.machine);

  return SUCCESS;
}

uint32_t get_timestamp(struct timespec * time, char * timestamp, uint32_t count)
{
  CHECK_NULL(time);
  CHECK_NULL(timestamp);

  // Create and write the timestamp
  snprintf(timestamp,
        count,
        "# Timestamp: %f\n",
        (double) time->tv_sec + (double) time->tv_nsec / 1000000000);

  return SUCCESS;
}

uint32_t create_dir(char * dir_name)
{
  FUNC_ENTRY;
  CHECK_NULL(dir_name);

  struct timespec dir_time;
  uint32_t res = 0;

  // Check for null pointer
  CHECK_NULL(dir_name);

  // Get the system time to append to directory to be created
  clock_gettime(CLOCK_REALTIME, &dir_time);

  // Log the newly create directory name
  LOG_LOW("Trying to create directory name: %s", dir_name);

  res = mkdir(dir_name, FILE_PERM);
  if (res == 0)
  {
    return SUCCESS;
  }
  else if (res == -1 && errno == EEXIST)
  {
    LOG_MED("%s directory already exists", dir_name);
    return SUCCESS;
  }
  else
  {
    LOG_ERROR("Could not create dir %s", dir_name);
    return FAILURE;
  }
} // create_dir()

/** @file capture.c
*
* @brief Holds the capture source
*
*/

#include <errno.h>
#include <fcntl.h>
#include <mqueue.h>
#include <pthread.h>
#include <sched.h>
#include <semaphore.h>
#include <stdint.h>
#include <stdlib.h>
#include <string.h>
#include <sys/types.h>
#include <sys/stat.h>
#include <sys/utsname.h>
#include <unistd.h>
#include <time.h>

#include "capture.h"
#include "log.h"
#include "profiler.h"
#include "project_defs.h"
#include "utilities.h"

// Use either JPEG or PPM to save files
#ifdef JPEG_COMPRESSION
#include "jpeg.h"
#include "server.h"
#else
#include "ppm.h"
#endif

// Warm up camera by capturing frames
#define WARM_UP
#define WARM_UP_FRAMES (10)

// Capture ping pong buffer size
#define CAP_BUF_SIZE (4)

// Open CV info
#define WINDOWNAME "capture"
#define DEVICE_NUMBER (0)

// Timing info
#define MICROSECONDS_PER_SECOND (1000000)
#define MICROSECONDS_PER_MILLISECOND (1000)

// Frame capture info
#define NUM_FRAMES (20)
#define PERIOD (100)
#define TIMING_BUFFER (125)

// Flag for stopping application. All services extern this variable.
uint32_t abort_test = 0;

// Ping Pong buffer for cap info
static cap_info_t cap_info[CAP_BUF_SIZE];

// Capture structure
static struct cap {
  CvCapture * capture;
  sem_t start;
  sem_t stop;
  mqd_t image_queue;
} cap;

/*!
* @brief Captures frames and passes them through a message queue for the
* jpeg/ppm service to convert and save to disk
* @param param void pointer to params
* @return NULL
*/
void * cap_service(void * param)
{
  FUNC_ENTRY;

  struct timespec time;
  struct timespec diff;
  cap_info_t * cur_cap_info;
  uint32_t count = 0;
  uint32_t res = 0;
  uint8_t timer = profiler_init();

  // Loop capturing frames and displaying
  while(!abort_test)
  {
    GET_TIME;
    DISPLAY_TIMESTAMP;
    // Wait for start signal
    sem_wait(&cap.start);
    START_TIME;

    // Get the time
    clock_gettime(CLOCK_REALTIME, &time);

    // Get the current cap info
    cur_cap_info = &cap_info[count % CAP_BUF_SIZE];

    EQ_RET_E(cur_cap_info->frame, cvQueryFrame(cap.capture), NULL, NULL);

    cur_cap_info->time = time;

    // Try to send the cap info via messaqe queue
    NOT_EQ_RET_EA(res,
        mq_send(cap.image_queue, (char *)cur_cap_info, sizeof(*cur_cap_info), 0),
        SUCCESS,
        NULL,
        abort_test);

    cvShowImage(WINDOWNAME, cur_cap_info->frame);
    cvWaitKey(1);

    // Post done
    sem_post(&cap.stop);
    count++;
  }
  LOG_HIGH("cap_service thread exiting");
  return NULL;
} // cap_service()

int sched_service()
{
  struct sched_param sched;
  struct sched_param cap_sched;
  struct timespec diff;
  pthread_t cap_thread;
  pthread_attr_t sched_attr;
  int32_t cap_policy = 0;
  int32_t res = 0;
  int32_t rt_max_pri = 0;
  uint8_t timer = profiler_init();

#ifdef WARM_UP
  // Frame used for capture during warm up phase
  IplImage * frame;
#endif // WARM_UP

  // Initialize log (does nothing if not using syslog)
  log_init();

  // Print function entry
  FUNC_ENTRY;

  // Unlink the queue name in case it is still hanging around, it is okay
  // if this fails it is just precaution for stale queues
  mq_unlink(QUEUE_NAME);

  // Create a window
  cvNamedWindow(WINDOWNAME, CV_WINDOW_AUTOSIZE);

  // Try to create the queue
  EQ_EXIT_E(cap.image_queue,
        mq_open(QUEUE_NAME, O_WRONLY | O_CREAT, S_IRWXU, NULL),
        -1);

  // Semaphore for timing
  PT_NOT_EQ_EXIT(res, sem_init(&cap.start, 0, 0), SUCCESS);
  PT_NOT_EQ_EXIT(res, sem_init(&cap.stop, 0, 0), SUCCESS);

  // Create a capture object and set values
  EQ_EXIT_E(cap.capture, (CvCapture *)cvCreateCameraCapture(DEVICE_NUMBER), NULL);

  // Initialize the schedule attributes
  PT_NOT_EQ_EXIT(res, pthread_attr_init(&sched_attr), SUCCESS);

  // Set the attributes structure to PTHREAD_EXPLICIT_SCHED and SCHED_FIFO
  PT_NOT_EQ_EXIT(res,
        pthread_attr_setinheritsched(&sched_attr, PTHREAD_EXPLICIT_SCHED),
        SUCCESS);
  PT_NOT_EQ_EXIT(res,
        pthread_attr_setschedpolicy(&sched_attr, SCHED_FIFO),
        SUCCESS);

  // Get the max priority
  EQ_EXIT_E(rt_max_pri, sched_get_priority_max(SCHED_FIFO), -1);

  // Set scheduler to SCHED_FIFO for the main thread
  sched.sched_priority = rt_max_pri;
  NOT_EQ_EXIT_E(res,
        sched_setscheduler(getpid(), SCHED_FIFO, &sched),
        SUCCESS);

  // Set the priority to max - 1 for the test thread
  sched.sched_priority = rt_max_pri - 1;
  PT_NOT_EQ_EXIT(res,
        pthread_attr_setschedparam(&sched_attr, &sched),
        SUCCESS);

  // Set resolution
  LOG_HIGH("Setting resolution to %dx%d", HRES, VRES);
  cvSetCaptureProperty(cap.capture, CV_CAP_PROP_FRAME_WIDTH, HRES);
  cvSetCaptureProperty(cap.capture, CV_CAP_PROP_FRAME_HEIGHT, VRES);

  // Create pthread
  PT_NOT_EQ_EXIT(res,
        pthread_create(&cap_thread, &sched_attr, cap_service, NULL),
        SUCCESS);

  // Get the scheduler parameters to display
  PT_NOT_EQ_EXIT(res,
        pthread_getschedparam(cap_thread, &cap_policy, &cap_sched),
        SUCCESS);
  LOG_HIGH("cap_thread policy: %d, priority: %d",
        cap_policy,
        cap_sched.sched_priority);

#ifdef JPEG_COMPRESSION
  // Try setting up the JPEG service
  NOT_EQ_EXIT_E(res, jpeg_init(), SUCCESS);
  // Try setting up the server service
  NOT_EQ_EXIT_E(res, server_init(), SUCCESS);
#else
  // Try setting up the ppm service
  NOT_EQ_EXIT_E(res, ppm_init(), SUCCESS);
#endif

#ifdef WARM_UP
  // Loop captures frames to allow camera to warm up
  LOG_MED("Running %d frames for warm up", WARM_UP_FRAMES);
  for (uint8_t frames = 0; frames < WARM_UP_FRAMES; frames++)
  {
    EQ_RET_E(frame, cvQueryFrame(cap.capture), NULL, FAILURE);
    cvShowImage(WINDOWNAME, frame);
    cvWaitKey(1);
    usleep(MICROSECONDS_PER_SECOND);
  }
#endif // WARM_UP

  // Loop captures frames to get stats
  for (uint32_t frames = 0; frames < NUM_FRAMES; frames++)
  {
    // Start the timer
    START_TIME;

    // Post semaphore for capture
    sem_post(&cap.start);

    // Get the time
    GET_TIME;

    // Display the time
    DISPLAY_TIMESTAMP;

    // Sleep for the period of a frame
    usleep(MICROSECONDS_PER_MILLISECOND * PERIOD - TIMING_BUFFER);

    // Start the timer
    START_TIME;

    if (!abort_test)
    {
      // Wait for frame to be captured
      sem_wait(&cap.stop);
    }
    else
    {
      break;
    }
    // Get the time
    GET_TIME;

    // Display the time
    DISPLAY_TIMESTAMP;
  }

  // Set the abort flag then allow the thread to exit
  sem_post(&cap.start);
  abort_test = 1;
  sem_post(&cap.stop);

  // Wait for test thread to join
  PT_NOT_EQ_EXIT(res,
        pthread_join(cap_thread, NULL),
        SUCCESS);
  LOG_MED("cap_service thread joined");

  // Destroy capture and window
  cvReleaseCapture(&cap.capture);
  cvDestroyWindow(WINDOWNAME);

  // Close the message queue fd
  mq_close(cap.image_queue);

  // Unlink it so it is destroyed
  mq_unlink(QUEUE_NAME);

  // Destroy log
  log_destroy();

  // Log capture thread exiting
  LOG_HIGH("sched_service exiting");
  return 0;
} // capture()

/** @file capture.h
*
* @brief Defines functions used for exercise3
*
*/

#ifndef __CAPTURE_H__
#define __CAPTURE_H__

#include <mqueue.h>

#include <opencv2/core/core.hpp>
#include <opencv2/highgui/highgui.hpp>
#include <opencv2/imgproc/imgproc.hpp>

// Max number for frames before unlinking old frames
#define MAX_FRAMES (2000)

typedef struct cap_info {
  IplImage * frame;
  struct timespec time;
} cap_info_t;

// Hold resolution information
typedef struct {
  uint32_t hres;
  uint32_t vres;
} resolution_t;

// Used for the image queue
typedef struct {
  mqd_t image_q;
  struct mq_attr attr;
} image_q_inf_t;

#define QUEUE_NAME "/frame_queue"

/*!
* @brief Starts capture, jpeg/ppm, and server service. Then becomes the
* scheduler service
* @return SUCCESS/FAILURE
*/
int sched_service();

#endif /* __CAPTURE_H__ */

/** @file utilities.h
*
* @brief Set of helpful utility functions
*
*/

#ifndef _UTILITIES_H
#define _UTILITIES_H

// File permissions used for saving files and creating directories
#define FILE_PERM (S_IRWXU | S_IRWXO | S_IRWXG)

uint32_t get_uname(char * uname_str, uint32_t count);
uint32_t get_timestamp(struct timespec * time, char * timestamp, uint32_t count);

/*!
* @brief Creates a new directory for new captures
* @param dirname pointer to buffer holding first part of directory name
* @param length length of buffer holding directory name
* @return SUCCESS/FAILURE
*/
uint32_t create_dir(char * dir_name);
#endif /* _UTILITIES_H */
/** @file jpeg.h
*
* @brief Exposes JPEG specific functionality
*
*/

#ifndef _JPEG_H
#define _JPEG_H

// Max timestamp length
#define TIMESTAMP_MAX (32)
#define DIR_NAME "capture_jpeg"

// Image Resolution information
#define HRES (640)
#define VRES (480)
#define BYTES_PER_PIXEL (3)
#define IMAGE_NUM_BYTES (HRES * VRES * BYTES_PER_PIXEL)

/*!
* @brief Start the jpeg_service thread
* @return SUCCESS/FAILURE
*/
uint32_t jpeg_init();
#endif /* _JPEG_H */

/** @file client.h
*
* @brief Holds functionality for socket client
*
*/

#ifndef _CLIENT_H
#define _CLIENT_H

/*!
* @brief Initialize client socket to talk to server
* @param sockfd pointer to a int32_t to hold socket fd after creation
* @return SUCCESS/FAILURE
*/
uint32_t client_init();

#endif /* _CLIENT_H */
/** @file profiler.h
*
* @brief Holds declarations for profiler
*
*/

#ifndef __PROFILER_H__
#define __PROFILER_H__

#include <stdint.h>
#include <stddef.h>
#include <time.h>

/*!
* @brief Initializes the profiler
*/
uint8_t profiler_init();

/*!
* @brief Starts the timer
* @return status SUCCESS/FAIL
*/
int8_t start_timer(uint8_t timer);

/*!
* @brief Stops the timer
* @return status SUCCESS/FAIL
*/
int8_t stop_timer(uint8_t timer);

/*!
* @brief Resets the timer
*/
void reset_timer(uint8_t timer);

/*!
* @brief Returns nanosecond time
* @param[in] diff Pointer to a timespec structure to fill out with second
* and nanosecond difference.
*/
void get_time(uint8_t timer, struct timespec * diff);

#endif // __PROFILER_H__
/** @file log.h
*
* @brief Defines items used in logging
*
*/

#ifndef __LOG_H__
#define __LOG_H__

#include <stdio.h>

// Logging level enumerations
typedef enum {
  LOG_LEVEL_HIGH,
  LOG_LEVEL_MEDIUM,
  LOG_LEVEL_LOW,
  LOG_LEVEL_ERROR,
  LOG_LEVEL_FATAL
} log_level_t;

/*!
* @brief Initializes the syslog
*/
void log_init();

/*!
* @brief Destroy syslog
*/
void log_destroy();

/*!
* @brief Log at a certain level
* @param[in] level logging level for this statement
* @param[in] p_filename pointer to the file name
* @param[in] p_function pointer to the function name
* @param[in] line_no line number in file
* @param[in] ... variadic arguments for printf
* @return pointer to the basename
*/
void log_level
(
  log_level_t level,
  char * p_filename,
  const char * p_function,
  uint32_t line_no,
  ...
);

#define LOG(level, ...) log_level(level, \
        (char *)__FILE__, \
        __FUNCTION__, \
        __LINE__, \
        __VA_ARGS__)

// Different log levels which can be turned on/off by setting LOG_LEVEL
#if LOG_LEVEL > 0
#define LOG_HIGH(...) LOG(LOG_LEVEL_HIGH, __VA_ARGS__)
#else
#define LOG_HIGH(...)
#endif /* LOG_LEVEL > 0 */

#if LOG_LEVEL > 1
#define LOG_MED(...) LOG(LOG_LEVEL_MEDIUM, __VA_ARGS__)
#else
#define LOG_MED(...)
#endif /* LOG_LEVEL > 1 */

#if LOG_LEVEL > 2
#define LOG_LOW(...) LOG(LOG_LEVEL_LOW, __VA_ARGS__)
#else
#define LOG_LOW(...)
#endif /* LOG_LEVEL > 2 */

// Function entry log. This should be placed at the beginning of each function
#define FUNC_ENTRY LOG_MED("Entering %s()", __FUNCTION__)

// Error and Fatal definitions. Fatal should be used sparingly and
// mostly debugging
#define LOG_ERROR(...) LOG(LOG_LEVEL_ERROR, __VA_ARGS__)
#define LOG_FATAL(...) LOG(LOG_LEVEL_FATAL, __VA_ARGS__)

#endif /* __LOG_H__ */
/** @file ppm.h
*
* @brief Exposes PPM specific functionality
*
*/

#ifndef _PPM_H
#define _PPM_H

// Max timestamp length
#define TIMESTAMP_MAX (40)

// Image Resolution information
#define HRES (640)
#define VRES (480)
#define BYTES_PER_PIXEL (3)
#define IMAGE_NUM_BYTES (HRES * VRES * BYTES_PER_PIXEL)

// Structure to overlay blue, green, and red
typedef struct colors {
  uint8_t blue;
  uint8_t green;
  uint8_t red;
} __attribute__((packed)) colors_t;

/*!
* @brief Start the ppm thread
* @return SUCCESS/FAILURE
*/
uint32_t ppm_init();
#endif /* _PPM_H */
/** @file server.h
*
* @brief Holds defintions for TCP server
*
*/

#ifndef __SERVER_H__
#define __SERVER_H__

#include "project_defs.h"

// Queue name for images to passed to be sent of TCP socket
# define SERVER_QUEUE_NAME "/server_queue"

// Structure holding information to be passed over TCP socket
typedef struct server_info {
  char file_name[FILE_NAME_MAX];
  uint32_t file_name_len;
  uint8_t * image_buf;
  uint32_t image_buf_len;
} server_info_t;

/*!
* @brief Starts a TCP server
* @return status SUCCESS/FAIL
*/
status_t server_init();

#endif /* __SERVER_H__ */
/** @file template.h
*
* @brief A description of the module’s purpose.
*
*/

#ifndef _TEMPLATE_H
#define _TEMPLATE_H

/*!
* @brief Identify the larger of two 8-bit numbers.
* @param[in] num1 The first number to be compared.
* @param[in] num2 The second number to be compared.
* @return int8_t
*/
int8_t max8(int8_t num1, int8_t num2);

#endif /* _TEMPLATE_H */
/** @file project_defs.h
*
* @brief Holds common project definitions
*
*/

#ifndef __PROJECT_DEFS_H__
#define __PROJECT_DEFS_H__

typedef enum status {
  SUCCESS,
  FAILURE
} status_t;

// Max file name
#define FILE_NAME_MAX (255)

// Helpful Macros
#define START_TIME start_timer(timer)
#define DISPLAY_TIMESTAMP LOG_FATAL("sec: %d, millisec: %f", \
        diff.tv_sec, \
        (float)(diff.tv_nsec)/1000000)

#define GET_TIME stop_timer(timer); \
        get_time(timer, &diff);

// Null pointer check
#define CHECK_NULL(x) if (x == NULL) { return FAILURE; }

// Check value not equal, print errno, and exit
#define NOT_EQ_EXIT_E(res, func, val) \
  if((res = func) != val) \
  { \
    LOG_ERROR(#func " failed with error: %s", strerror(errno)); \
    exit(1); \
  }

// Check value not equal, print errno, and return failure
#define NOT_EQ_RET_E(res, func, val, ret) \
  if((res = func) != val) \
  { \
    LOG_ERROR(#func " failed with error: %s", strerror(errno)); \
    return ret; \
  }

// Check value equal, print errno, and return failure
#define EQ_RET_E(res, func, val, ret) \
  if((res = func) == val) \
  { \
    LOG_ERROR(#func " failed with error: %s", strerror(errno)); \
    return ret; \
  }

// Check value not equal, print errno, set abort, and return a value
#define NOT_EQ_RET_EA(res, func, val, ret, abort) \
  if((res = func) != val) \
  { \
    LOG_ERROR(#func " failed with error: %s", strerror(errno)); \
    abort = 1; \
    return ret; \
  }

// Check value equal, print errno, set abort, and return a value
#define EQ_RET_EA(res, func, val, ret, abort) \
  if((res = func) == val) \
  { \
    LOG_ERROR(#func " failed with error: %s", strerror(errno)); \
    abort = 1; \
    return ret; \
  }

// Check value equal, print errno, and return failure
#define EQ_EXIT_E(res, func, val) \
  if((res = func) == val) \
  { \
    LOG_ERROR(#func " failed with error: %s", strerror(errno)); \
    exit(1); \
  }

#define PT_NOT_EQ_RET(res, func, val, ret) \
  if((res = func) != val) \
  { \
    LOG_ERROR(#func " failed with error: %s", strerror(res)); \
    return ret; \
  }

#define PT_EQ_RET(res, func, val, ret) \
  if((res = func) == val) \
  { \
    LOG_ERROR(#func " failed with error: %s", strerror(res)); \
    return ret; \
  }

#define PT_NOT_EQ_EXIT(res, func, val) \
  if((res = func) != val) \
  { \
    LOG_ERROR(#func " failed with error: %s", strerror(res)); \
    exit(res); \
  }

#endif /* __PROJECT_DEFS_H__ */